## Slide 1: Using SIMetrix/SIMPLIS to address the PDN problem– when powering microprocessors with high di/dt loads
SIMPLIS Technologies
June 2024

## Slide 2: Simulation schematic of a synchronous-rectified buck converter
PDN

## Slide 3: Example VRM with PDN connected load

## Slide 4: The PDN problem
…
…
…
…
Controller
Physical Output Capacitors
mounted on the PCB
…
Printed
Circuit
Board (PCB)
Layout
Socket
&
Package -or-
Test
Fixture
Power
Stage
VRM
VLoad
CPU/
GPU/
MCU/
FPGA
Load

## Slide 5: The PDN problem from the Mother Board designer perspective.
…
…
…
Physical Output Capacitors
mounted on the PCB
…
Power
Stage
VRM
PDN
Printed
Circuit
Board (PCB)
Layout
…
Socket
&
Package -or-
Test
Fixture
VLoad
CPU/
GPU/
MCU/
FPGA
Load
Controller
PDN

## Slide 6: The PDN problem from the Mother Board perspective.
…
…
…
Physical Output Capacitors
mounted on the PCB
…
Power
Stage
VRM
PDN
Printed
Circuit
Board (PCB)
Layout
…
Socket
&
Package -or-
Test
Fixture
VLoad
CPU/
GPU/
MCU/
FPGA
Load
Controller
∆ iLoad ~ 1000 A
d iLoad/dt ~ 1A/ns
PDN

## Slide 7: The PDN problem from the Mother Board perspective.
…
…
…
Physical Output Capacitors
mounted on the PCB
…
Power
Stage
VRM
PDN
Printed
Circuit
Board (PCB)
Layout
…
Socket
&
Package -or-
Test
Fixture
VLoad
CPU/
GPU/
MCU/
FPGA
Load
Controller
∆ iLoad ~ 1000 A
d iLoad/dt ~ 1A/ns
VOSENP
PDN

## Slide 8: The PDN problem from the Mother Board perspective.
…
…
…
Physical Output Capacitors
mounted on the PCB
…
Power
Stage
VRM
PDN
Printed
Circuit
Board (PCB)
Layout
…
VLoad
Controller
∆ iLoad ~ 1000 A
d iLoad/dt ~ 1A/ns
VOSENP
Test
Fixture
Load
PDN

## Slide 9: The PDN problem from the Mother Board perspective.
…
…
…
Physical Output Capacitors
mounted on the PCB
…
Power
Stage
VRM
PDN
Printed
Circuit
Board (PCB)
Layout
…
VLoad
Controller
∆ iLoad ~ 1000 A
d iLoad/dt ~ 1A/ns
VOSENP
Test
Fixture
Load
PDN

## Slide 10: The PDN problem from the Mother Board perspective.
…
…
…
Physical Output Capacitors
mounted on the PCB
…
Power
Stage
VRM
PDN
…
VLoad
Controller
∆ iLoad ~ 1000 A
d iLoad/dt ~ 1A/ns
VOSENP
Test
Fixture
Load
Printed
Circuit
Board (PCB)
Layout
PDN

## Slide 11: The PDN problem
The large difference between the Load current
and
Total of all phase currents from the Power Stage
requires large amount of capacitive energy-storage to limit ∆ VOSENP within spec
The very
high di/dt of the Load
causes voltage drop across parasitic inductance of PDN

## Slide 12
The large difference between the Load current
and
Total of all phase currents from the Power Stage
requires large amount of capacitive energy-storage to limit ∆ VOSENP within spec
The very
high di/dt of the Load
causes voltage drop across parasitic inductance of PDN
The PDN problem is a time-domain problem

## Slide 13: The PDN problem –
The large difference between the Load current
and
Total of all phase currents from the Power Stage
requires large amount of capacitive energy-storage to limit ∆ VOSENP within spec
The very
high di/dt of the Load
causes voltage drop across parasitic inductance of PDN
simulation is the only
practical solution

## Slide 14: The PDN simulation process Mother Board designer’s perspective
Extract Spice netlist of PDN from PCB layout
Convert PDN Netlist to SIMPLIS and SIMetrix Compatible Netlists and Create Associated Symbol
Using SIMetrix PDN test bench, characterize performance of Full PDN and R-Only PDN using worst-case expected load-transient current waveform
Using SIMetrix testbench:
  Find optimum curve-fit values for Reduced-Order PDN model
  Compare performance of Full, R-Only, and the Reduced-Order PDN models with worst-case expected load-transient current waveform
Using SIMPLIS testbench with complete SIMPLIS converter model:
  Compare system performance of R-Only, and Reduced-Order (and possibly Full) PDN models

## Slide 15: What is inside a typical PDN model of PCB layout?
Hundreds to thousands of equivalent resistors, inductors, and capacitors
Too many L’s and C’s will dramatically slow SIMPLIS down, since it pays attention to every inductor and capacitor
Proposing a simulation process
  Accurate enough to be reliable and fast enough to be practical

## Slide 16: Step #1a: Identify the ports of the PDN

## Slide 17: Step #1a: Identify the ports of the PDN
Limit to no more than 10 to
12 ports
Group capacitors into islands –
by location on the PCB

## Slide 18: Step #1b: Use Multi-Level Capacitors with Quantity

## Slide 19: Step #1c: Extract SPICE netlist of PDN from PCB layout
Use a tool that can generate s-parameter data between ports from the layout description
  Do NOT include the bulk (physical) capacitors as part of the PDN
Use another tool to extract SPICE model (netlist) of PDN from PCB layout s-parameter data
  Make sure to check for passivity
  Make sure to meet causality requirement
  For starter, set maximum number of poles (order) to 100
These tools are not provided by SIMPLIS Technologies

## Slide 20: Step #2: Access the Parse PDN Netlist tool by clicking Tools > Parse PDN Netlist
The Parse PDN Netlist tool is only accessible when the schematic is in SIMPLIS mode

## Slide 21: Step #2: Use the SIMPLIS Parse PDN NetList Tool
To create a library file that supports the SIMPLIS simulator as well as the SIMetrix simulator
  Each simulator will have a Resistive-only (R_only) model for the PDN
  Each simulator will have a Full model of the PDN
To create a symbol representing the PDN for use in SIMetrix/SIMPLIS

## Slide 22: Specifying the generated library to be included in the simulation
Open the F11 window by hitting the F11 key
Copy and paste a line from the command shell window as shown in Application G in SIMPLIS Advanced Training material

## Slide 23: Choosing between the R_only model and the Full model for the PDN
Double clicking the symbol brings up a GUI dialog to choose the PDN model
The R_only model is the default mode when you place the symbol on the schematic

## Slide 24: The PDN Simulation Problem
Even with a “reasonably sized” PDN
In this example,
the Full PDN model takes ~ 15 - 20x times longer to simulate than with the R_only PDN model
Show how to approximate the Full PDN model in a way maintains required accuracy but still runs fast.
  Reduced Order PDN model

## Slide 25: Step #3: Use SIMetrix testbench to characterize the PDN
Only models the PDN, bulk caps, and load current
VRM phases replaced by a 1.8 V voltage source
One PDN is selected to use the R_only model and the other is set to use the Full model
Run transient simulations and compare the output at VOSENP

## Slide 26
Step #3:
SIMetrix testbench

## Slide 27: Compare voltage at the VOSENP node between two models of PDN
This difference is caused by parasitic inductance of PCB layout
Ringing is caused by interaction w/ parasitic capacitance

## Slide 28: Step #4a Use Optimizer to find Reduced-Order PDN Model

## Slide 29
1) Manually estimate reasonable starting for values of L1_R, L2_R, R1_R, and R5_R
2) Use SIMetrix optimizer to refine the values of L1_R, L2_R, R1_R, and R5_R
Step #4a Use Optimizer to find Reduced-Order PDN Model

## Slide 30: Step #4b Compare results of Optimization
Agreement between VOSENP_Full and VOSENP_Reduced is impressive!

## Slide 31: Zoomed in comparison

## Slide 32: Zoomed in comparison
Further improvement can be achieved by adding capacitance to Reduced Order model

## Slide 33: Step #4a Reduced-Order PDN Model w/ Capacitance
1) With fixed “optimum” values
of L1_R, L2_R, R1_R, and R5,
2) Use SIMetrix optimizer to find values of R3_R and C13_R

## Slide 34: Zoomed in comparison of VOSENP with Reduced Order model with RC

## Slide 35: Can follow the same process with vLoad_P with Reduced Order model with RC

## Slide 36: The PDN simulation process Mother Board designer’s perspective
Extract Spice netlist of PDN from PCB layout
Convert PDN Netlist to SIMPLIS and SIMetrix Compatible Netlists and Create Associated Symbol
Using SIMetrix PDN test bench, characterize performance of Full PDN and R-Only PDN using worst-case expected load-transient current waveform
Using SIMetrix testbench:
  Find optimum curve-fit values for Reduced-Order PDN model
  Compare performance of Full, R-Only, and the Reduced-Order PDN models with worst-case expected load-transient current waveform
Using SIMPLIS testbench with complete SIMPLIS converter model:
  Compare system performance of R-Only, and Reduced-Order (and possibly Full) PDN models

## Slide 37: Step #5: Insert Reduced-Order Model of PDN into SIMPLIS testbench

## Slide 38: Compare SIMPLIS results from simulations using different PDN models
R_only Model: R_only PDN library model with no added external L/R
Reduced-Order Model: R_only PDN library model with added external L/R and RC
Full Model: Full PDN library model

## Slide 39
Compare SIMPLIS results from 3 PDN models:
R_only
Reduced_w_RC
Full

## Slide 40
Compare results from 3 PDN models:

## Slide 41: Comparison of CPU run times

## Slide 42: Observations
For a well designed PCB, the Reduced Order PDN model can be sufficient for
    AC analysis: Bode Plots for stability analysis, Zout
    Output Capacitor selection: Number, type and location
    Step Load Transients: Output voltage transients with high di/dt
    Controller & Load step interactions: Repeated step load transients
Still want to do some judicious verification with Full PDN model
R_only PDN model good for
    Initial simulation set up
    Preliminary design
    Stability analysis

## Slide 43: How do you avoid the rouge wave problem?
Avoid creating a PDN with resonant peaks in Zout
BUT, a VRM is not a linear system

## Slide 44: Output Impedance Zout
The Reduced Order PDN model agrees very well with Full PDN
Zout beyond ~ 1 – 10 MHz is dominated by Socket and Package impedance

## Slide 45: How do you avoid the rouge wave problem?
Avoid creating a PDN with resonant peaks in Zout
BUT, a VRM is a nonlinear system
  Controller & Power Stage are very nonlinear
    Still need to stress test this combination
      Large-signal time-domain response to extreme repeated load pulses
    Show DVM results

## Slide 46
Pulse Load steps
151 frequencies (1 kHz – 1 MHz) and
9 duty ratios (10% - 90%)
1359 step load simulations
Controller & Power Stage
Stress Test
The PDN problem is a time-domain problem

## Slide 47
Controller & Power Stage
Stress Test
The PDN problem is a time-domain problem